## Slide 1: UCM Simulator Test Framework
Contains confidential proprietary and trade secrets information of CNH Industrial. Any use of this work without express written consent is strictly prohibited.
May 24th, 2019
Python based testing of UCM functionality
Koen Taillaert
Zedelgem, Belgium

## Slide 2: Contents
Overview
UCM simulator functions
Camel functions
Python and IDE setup
Examples

## Slide 3
Camel
Windows Simulation
Vehicle Code
App DLL Wrapper
UCMSimFramework DLL
Callback API
Configuration
I/O Controls
Vector
PCAN
CanSim
Application DLL
Simulation EXE
Plant models
API
CanGateway
Dspace
XIL
XIL2UCM
API
Python
UCMSimTest

## Slide 4: UCM Simulator Test Framework Interface
Interface: JSON over Windows Named Pipe
UCM simulator for IO access
CAMEL Tool for CAN data
Interface documentation: https://repo.cnhind.com/svn/harvester_libraries/UCMSimFramework/trunk/TestFramework/doc/Ucm_simulation_external_test_framework.docx
Python Test Framework using this interface
  UCM simulator and Camel Tool must be running and configured
  https://repo.cnhind.com/svn/harvester_libraries/UCMSimFramework/trunk/TestFramework/doc/Ucm_simulation_python_test_env.docx
General Overview

## Slide 5: UCM simulator functions
Detailed description in https://repo.cnhind.com/svn/harvester_libraries/UCMSimFramework/trunk/TestFramework/doc/Ucm_simulation_python_test_env.docx
Setting IO
  Different functions for IO Types (analog, switch, frequency, …) cf. UI types
    set_io_voltage(spn, voltage)
    set_io_frequency(spn, voltage, frequency)
    set_io_pulse(spn, voltage, pulses)
    set_io_switch(spn, boolean)
    set_io_pwm(spn, voltage, period, duty)
Setting IO

## Slide 6: UCM simulator functions
Getting IO
  Last received IO value is stored in spnlist table
    Table 6 - SpnList functionality per input/output type
  Set command triggers response with value
  get_io_data(spn) : requests SPN data from UCM sim
  io_subscribe(spn) : UCM sim sends new value when changed
    io_unsubscribe(spn)
  set_callback_function(spn, callback)
    when spn value received: executes callback function
    remove_callback_function(spn)
Getting IO

## Slide 7: UCM simulator functions
function | Voltage Input | Frequency Input | Pulse Input | Digital Input | PWM Input | Digital Output | PWM Output
all_data(spn) | V | V | V | V | V | V | V
remove(spn) | V | V | V | V | V | V | V
type(spn) (*2) | V | V | V | V | V | V | V
voltage(spn)(*1) | V | V | V | V(*4) | V | V | 
frequency(spn) (*1) |  | V |  |  |  |  | 
increment(spn) (*1) |  |  | V |  |  |  | 
period(spn) (*1) |  |  |  |  | V |  | 
duty(spn) (*1) |  |  |  |  | V |  | V
switch(spn) (*1) |  |  |  | V(*5) |  |  | 
current(spn) (*1) |  |  |  |  |  | V | V
error(spn) (*3) | V | V | V | V | V | V | V
SpnList functionality
Table 6 - SpnList functionality per input/output type
(*1) Return value is according to Table 5 – UCM input function overview
(*2) Return value is according to type value from Table 3 - UCM supported input types and Table 4 - UCM supported output types
(*3) returns “none” when no error is recorded, otherwise error text as per protocol spec[1]
(*4) Valid only after set_io_voltage or get_io_data call
(*5) Valid only after set_io_switch or get_io_data call

## Slide 8: UCM simulator functions
Custom command pass through
  Write your own plant model controls
  Register Callback from UCM sim application
    UCM sim: FrameworkCore.ExternalTestModule.RegisterReceivedDataCallback
    Python: Use send_message(string,string,float,float,float,float) function to send messages
    Bypass commands from Ucm_simulation_external_test_framework.docx Table 4
Example from sugarcane
Custom commands

## Slide 9: Camel functions
Referenced by CAN DB signal name
  SignalId : bus number, source address, message name, signal name
    flash_indic = SignalId(CAN_BUS_1, 0x80, 'ucm1_status', 'flash_indicator')
  Last value is stored in SignalList table
  set_signal_value(sigid, value)
    Also triggers response
  get_signal_value(sigid)
  signal_subscribe(sigid): subscribe to CAN signal.
    signal_unsubscribe(sigid)
  set_signal_callback_function(sigid, callback)
    when can value received: executes callback function
    remove_signal_callback_function(sigid)
Signal based

## Slide 10: Camel functions
Referenced by PGN
  Raw can data
  PgnId: bus number, source addr, PGN, (optional multiplex)
  Last value is stored in PgnList table
  set_pgn_data(pgngid, value)
    Also triggers response
  get_pgn_data(pgnid)
PGN based

## Slide 11: Camel functions
CCS settings
  Referenced by CCS setting id
  set_ccs_value(ccs_id, value) : set the value of the setting
    Camel will send 0xCC token with SA 0x90
  get_ccs_value(ccs_id): get the value of the setting
  Last value is stored in CCSList table
    ccs_list.value(ccs_id)
CCS settings

## Slide 12: Python requirements
Python :
  Minimum version required: Python 3.5 (https://www.python.org/downloads/)
  Pywin32 (minimum version 244) (https://pypi.org/project/pywin32/
  Pytest (minimum version 4.0.2) (https://docs.pytest.org/en/latest/getting-started.html
IDE development :
  Easy development and Python setup
  PyCharm Community Edition (https://www.jetbrains.com/pycharm/)
Cmd line deployment :
  For automatic testing
  Needs ntlm proxy setup (http://cntlm.sourceforge.net/) to work on CNHI network

## Slide 13: Installation for IDE development
Install Python :
  Minimum version required: Python 3.5
  https://www.python.org/downloads/
Install PyCharm Community Edition :
  https://www.jetbrains.com/pycharm/

## Slide 14: PyCharm IDE setup
File  New Project
Create Project

## Slide 15: PyCharm IDE setup
File  Settings Project Project Interpreter
Install «pywin32» and «pytest»
Install modules

## Slide 16: PyCharm IDE setup
File  Settings  Appearance & Behavior  System Settings  HTTP Proxy  Auto-detect proxy settings
Proxy configuration

## Slide 17: PyCharm IDE setup
File  Settings  Tools Python Integrated Tools Testing Default test runner  pytest
Pytest integration

## Slide 18: Test development in IDE
Copy UCMSimTest in the project
  https://repo.cnhind.com/svn/harvester_libraries/UCMSimFramework/trunk/TestFramework/UCMSimTest
Add UCMSimTest

## Slide 19: Test development in IDE
Copy conftest.py in the project (pytest configuration file example)
  https://repo.cnhind.com/svn/harvester_libraries/UCMSimFramework/trunk/TestFramework/example/conftest.py
Add conftest.py

## Slide 20: Test development in IDE
Run 1 test, or all tests from UI by pressing green arrow next to class (all tests) or 1 specific test,
Run from UI

## Slide 21: Test development in IDE
Run via built-in terminal
Run from terminal

## Slide 22: Pytest
Full documentation available at https://docs.pytest.org/en/latest/
“pytest” will run all files of the form test_*.py or *_test.py in the current directory and its subdirectories
Create xml output
  pytest --junitxml=report.xml
For html reports: install «pytest-html» package
  pytest --html=report.html
  https://pypi.org/project/pytest-html/
Advanced example:
  https://repo.cnhind.com/svn/sugarcaneharvester/trunk/test

## Slide 23: Conftest.py example
Import statements
Execute once to set up environment
Execute once after all tests have been executed (“yield”) to clean up environment
Configure the test environment: set up connections to the Simulator(s) and Camel Tool

## Slide 24: Conftest.py example
PipeManager('UCMSimPipeSetApplication_UCM1_CX56.dll‘, 'UCMSimPipeGetApplication_UCM1_CX56.dll')
  Sets up connection to UCM simulator
  Create multiple PipeManagers to use multiple UCM simulators simultaneously
UcmCommand(self.ucm_pipe_manager.connect_sender(), self.ucm_pipe_manager.connect_receiver())
  Connects UCM command module to the pipes
SpnList(self.ucm_command)
  Links the UCM command module to the SpnList
PipeManager('CamelPipeSet', 'CamelPipeGet')
  Sets up connection to Camel Tool
  Only 1 Camel tool connection possible
CamelCommand(self.camel_pipe_manager.connect_sender(), self.camel_pipe_manager.connect_receiver())
  Connects Camelcommand module to the pipes
SignalList(self.camel_command)
  Links the UCM command module to the SignalList
CcsList(self.camel_command)
  Links the UCM command module to the SignalList
https://repo.cnhind.com/svn/harvester_libraries/UCMSimFramework/trunk/TestFramework/doc/Ucm_simulation_external_test_framework.docx
Setting up the connections

## Slide 25: Test example
Link to Setup & Teardown cf conftest.py
Subscribe to the flash indicator signal
Set all required IO
Give time for CAN signal to be set
Unsubscribe the can signal
Check if signal has expected value

## Slide 26: Test example failure

## Slide 27: Executing tests
Camel Tool and UCM simulator must be running and configured
Switch off in Camel Tool:
  CCS Master mode
  Cyclic can messages (for nodes that are controlled by UCM sim)